Chapter 4
Gates and Circuits

---
Layers of a Computing System
Layers of a Computing System
Communication
Application
Operating System
Programming
Hardware
Information

---
Chapter Goals
Identify the basic gates and describe the behavior of each
Describe how gates are implemented using transistors
Combine basic gates into circuits
Describe the behavior of a gate or circuit using Boolean expressions, truth tables, and logic diagrams

---
Computers and Electricity
Gate - A device that performs a basic operation on electrical signals
Circuits - Gates combined to perform more complicated tasks

---
Computers and Electricity
There are three different, but equally powerful, notational methods
for describing the behavior of gates
and circuits
  - Boolean expressions
  - logic diagrams
  - truth tables

---
Computers and Electricity
Boolean expressions Expressions in Boolean algebra, a mathematical notation for expressing two-valued logic
This algebraic notation is an elegant and powerful way to demonstrate the activity of electrical circuits

---
Computers and Electricity
Logic diagram A graphical representation of a circuit
  - Each type of gate is represented by a specific graphical symbol
Truth table A table showing all possible input value and the associated output values

---
Gates
Let’s examine the processing of the following
six types of gates
  - NOT
  - AND
  - OR
  - XOR
  - NAND
  - NOR
Typically, logic diagrams are black and white, and the gates are distinguished only by their shape

---
NOT Gate
A NOT gate accepts one input value
and produces one output value
Figure 4.1 Various representations of a NOT gate

---
NOT Gate
By definition, if the input value for a NOT gate is 0, the output value is 1, and if the input value is 1, the output is 0
A NOT gate is sometimes referred to as an inverter because it inverts the input value

---
AND Gate
An AND gate accepts two input signals
If the two input values for an AND gate are both 1, the output is 1; otherwise, the output is 0
Figure 4.2 Various representations of an AND gate

---
OR Gate
If the two input values are both 0, the output value is 0; otherwise, the output is 1
Figure 4.3 Various representations of a OR gate

---
XOR Gate
XOR, or exclusive OR, gate
  - An XOR gate produces 0 if its two inputs are the same, and a 1 otherwise
  - Note the difference between the XOR gate
    and the OR gate; they differ only in one
    input situation
  - When both input signals are 1, the OR gate produces a 1 and the XOR produces a 0

---
XOR Gate
Figure 4.4 Various representations of an XOR gate

---
NAND and NOR Gates
The NAND and NOR gates are essentially the opposite of the AND and OR gates, respectively
Figure 4.5 Various representations of a NAND gate
Figure 4.6 Various representations of a NOR gate

---
Review of Gate Processing
A NOT gate inverts its single input value
An AND gate produces 1 if both input values are 1
An OR gate produces 1 if one or the other or both input values are 1

---
Review of Gate Processing
An XOR gate produces 1 if one or the other (but not both) input values are 1
A NAND gate produces the opposite results of an AND gate
A NOR gate produces the opposite results of an OR gate

---
Gates with More Inputs
Gates can be designed to accept three or more input values
A three-input AND gate, for example, produces an output of 1 only if all input values are 1
Figure 4.7 Various representations of a three-input AND gate

---
Constructing Gates
Transistor A device that acts, depending on the voltage level of an input signal, either as a wire that conducts electricity or as a resistor that blocks the flow of electricity
  - A transistor has no moving parts, yet acts like
    a switch
  - It is made of a semiconductor material, which is neither a particularly good conductor of electricity, such as copper, nor a particularly good insulator, such as rubber

---
Tube & Transistors

---
Constructing Gates
A transistor has three terminals
  - A source
  - A base
  - An emitter, typically connected to a ground wire
If the electrical signal is grounded (base is high), it is allowed to flow through an alternative route to the ground (literally) where it can do no harm (source is low), otherwise source is high (+5V)
+5V
Figure 4.8 The connections of a transistor

---
Constructing Gates
It turns out that, because the way a transistor works, the easiest gates to create are the NOT, NAND, and NOR gates
Figure 4.9 Constructing gates using transistors

---
Getting Personal
McCulloch & Pitts – 1943, Artificial Neurons

---
Perceptron
Rosenblatt, 1962 – Perceptron Learning paper generates great interest
Minsky and Papert, 1969 – Computational Geometry proof starts a 20 year hiatus in Artificial Intelligence

---
“my brain hurts!”

---
Homework
Read Chapter Four, Sections 4.1 – 4.3
Exercise: P117, 18-29

---
Assignment One
Due Today, Wednesday
  - No lateness

---
Next Class
No Class Monday
Next Class is Wednesday, 10/4
Have a Nice Weekend...