Chapter 4
Gates and Circuits

---
Layers of a Computing System
Layers of a Computing System
Communication
Application
Operating System
Programming
Hardware
Information

---
Chapter Goals
Compare and contrast a half adder
and a full adder
Describe how a multiplexer works
Explain how an S-R latch operates
Describe the characteristics of the four generations of integrated circuits

---
Gates
Let’s examine the processing of the following
six types of gates
  - NOT
  - AND
  - OR
  - XOR
  - NAND
  - NOR
Typically, logic diagrams are black and white, and the gates are distinguished only by their shape

---
NOT Gate
A NOT gate accepts one input value
and produces one output value
Figure 4.1 Various representations of a NOT gate

---
NOT Gate
By definition, if the input value for a NOT gate is 0, the output value is 1, and if the input value is 1, the output is 0
A NOT gate is sometimes referred to as an inverter because it inverts the input value

---
AND Gate
An AND gate accepts two input signals
If the two input values for an AND gate are both 1, the output is 1; otherwise, the output is 0
Figure 4.2 Various representations of an AND gate

---
OR Gate
If the two input values are both 0, the output value is 0; otherwise, the output is 1
Figure 4.3 Various representations of a OR gate

---
XOR Gate
XOR, or exclusive OR, gate
  - An XOR gate produces 0 if its two inputs are the same, and a 1 otherwise
  - Note the difference between the XOR gate
    and the OR gate; they differ only in one
    input situation
  - When both input signals are 1, the OR gate produces a 1 and the XOR produces a 0

---
XOR Gate
Figure 4.4 Various representations of an XOR gate

---
NAND and NOR Gates
The NAND and NOR gates are essentially the opposite of the AND and OR gates, respectively
Figure 4.5 Various representations of a NAND gate
Figure 4.6 Various representations of a NOR gate

---
Review of Gate Processing
A NOT gate inverts its single input value
An AND gate produces 1 if both input values are 1
An OR gate produces 1 if one or the other or both input values are 1

---
Review of Gate Processing
An XOR gate produces 1 if one or the other (but not both) input values are 1
A NAND gate produces the opposite results of an AND gate
A NOR gate produces the opposite results of an OR gate

---
Homework
Read Chapter Four, Sections 4.1 – 4.3
Exercise: P117, 18-29

---
Constructing Gates
A transistor has three terminals
  - A source
  - A base
  - An emitter, typically connected to a ground wire
If the electrical signal is grounded (base is high), it is allowed to flow through an alternative route to the ground (literally) where it can do no harm (source is low), otherwise source is high (+5V)
+5V
Figure 4.8 The connections of a transistor

---
Constructing Gates
It turns out that, because the way a transistor works, the easiest gates to create are the NOT, NAND, and NOR gates
Figure 4.9 Constructing gates using transistors

---
Circuits
Two general categories
  - In a combinational circuit, the input values explicitly determine the output
  - In a sequential circuit, the output is a function of the input values as well as the existing state of the circuit
As with gates, we can describe the operations
of entire circuits using three notations
  - Boolean expressions
  - logic diagrams
  - truth tables

---
Combinational Circuits
Gates are combined into circuits by using the output of one gate as the input for another

---
Combinational Circuits
Because there are three inputs to this circuit, eight rows are required to describe all possible input combinations
This same circuit using Boolean algebra is (AB + AC)

---
Now let’s go the other way; let’s take a Boolean expression and draw
Consider the following Boolean expression A(B + C)
Now compare the final result column in this truth table to the truth table for the previous example
They are identical

---
Now let’s go the other way; let’s take a Boolean expression and draw
We have therefore just demonstrated circuit equivalence
  - That is, both circuits produce the exact same output for each input value combination
Boolean algebra allows us to apply provable mathematical principles to help us design
logical circuits

---
Properties of Boolean Algebra

---
Adders
At the digital logic level, addition is performed in binary
Addition operations are carried out
by special circuits called, appropriately, adders

---
Adders
The result of adding two binary digits could produce a carry value
Recall that 1 + 1 = 10
in base two
A circuit that computes the sum of two bits
and produces the correct carry bit is called a half adder

---
Adders
Circuit diagram representing
a half adder
Two Boolean expressions:
sum = A  B
carry = AB

---
Adders
A circuit called a full adder takes the carry-in value into account
Sum of two binary values with multiple digits each

---
Multiplexers
Multiplexer is a general circuit that produces a single output signal
  - The output is equal to one of several input signals to the circuit
  - The multiplexer selects which input signal is used as an output signal based on the value represented by a few more input signals, called select signals or select control lines
  - animation_telephony_mux_slow.gif
  - http://en.wikipedia.org/wiki/Multiplexers

---
Multiplexers
The control lines S0, S1, and S2
determine which of eight other input lines
(D0 through D7) are routed to the output (F)
Figure 4.11 A block diagram of a multiplexer with three select control lines

---
Circuits as Memory
Digital circuits can be used to store information
These circuits form a sequential circuit, because the output of the circuit is also used as input to the circuit

---
Circuits as Memory
An S-R latch stores a single binary digit
(1 or 0)
There are several ways an S-R latch circuit could be designed using various kinds of gates
http://en.wikipedia.org/wiki/Flip-flop_%28electronics%29

---
Circuits as Memory
The design of this circuit guarantees that the two outputs X and Y are always complements of each other
The value of X at any point in time is considered to be the current state of the circuit
Therefore, if X is 1, the circuit is storing a 1; if X is 0, the circuit is storing a 0
Figure 4.12 An S-R latch

---
Integrated Circuits
Integrated circuit (also called a chip) A piece of silicon on which multiple gates have been embedded
These silicon pieces are mounted on a plastic or ceramic package with pins along the edges that can be soldered onto circuit boards or inserted into appropriate sockets

---
Integrated Circuits
Figure 4.13 An SSI chip contains independent NAND gates

---
Integrated Circuits
Integrated circuits (IC) are classified by the number of gates contained in them
Wafer Scale Integration

---
CPU Chips
The most important integrated circuit
in any computer is the Central Processing Unit, or CPU
Each CPU chip has a large number
of pins through which essentially all communication in a computer system occurs

---
Assignment One
Let Me Know If I Can Publish On Web Site
There No Obligation

---
Homework
Read Chapter Four, Sections 4.4 – 4.7
Exercise: P119-120, 55 & 59

---
Mid-Term
Take Home Exam – Non-Trivial (think!)
Cover Chapters 1-5 & 16 & Anything Covered In Class
Given Out: Oct 11
Due Back: Oct 18
No Lateness!!!

---
Good Night